## Slide 1: Factors Influencing Opportunistic Premise Plumbing Pathogens in Homes Joseph O. Falkinham, III jofiii@vt.edu
www.webbertraining.com
September 21, 2023

## Slide 2: Opportunistic Premise Plumbing Pathogens (OPPPs)
Normal inhabitants of natural waters and soils
Enter drinking water via treatment plants
Colonists, not contaminants
Treatment selects for OPPPs
Survive, grow, persist in drinking water
Infect individuals with risk factors

## Slide 3: Risk Factors for OPPP Lung Infection
Occupational Dust Exposure
Surgical Exposure (OR or ICU)
Prior Lung Infection
Genetic (Cystic Fibrosis)
Older, Slender, Taller Women (risk ?)

## Slide 4: OPPPs
Legionella pneumophila
Pseudomonas aeruginosa
Mycobacterium avium complex
Acinetobacter baumannii
Sphingomonas paucimobilis
Stenotrophomonas maltophilia
Cupriavidus spp.
Acanthamoeba polyphaga

## Slide 5: OPPP Characteristics
Disinfectant-Resistance
Prefer to Adhere to Surfaces
Form Biofilms on Surfaces
Grow at Low Organic Carbon
Grow at Low Oxygen (stagnation)
Concentrated in Aerosols
Grow in Amoebae
Desiccation-Tolerant

## Slide 6: Adherence and Biofilm Formation
Adherence Driven by Hydrophobicity
Growth of Adherent Cells = Biofilm
Protective Extracellular Matrix
Residence and Persistence
Resistance to Disinfection and Washout
Re-appearance Following Disinfection

## Slide 7: NTM in Household Plumbing
Enter Plumbing Through Municipal Pipe
Grow in Water Heater
Transported Throughout House
Attach to Surfaces Form Biofilm
Aerosolized in Showers, Taps, Drains
Grow in Stagnant Water

## Slide 8: Reducing OPPP Exposure -1
Raise Water Heater Temperature-130 F
Showerhead with Large Diameter Holes
Increase Bathroom Ventilation
No Direct Water Flow into Drains
Remove Aerators on Taps
Flush Before Collecting Water

## Slide 9: Reducing OPPP Exposure - 2
Disinfect Showerhead
Don’t Drink Refrigerator Water or Ice
Only Use Evaporative Humidifier
Avoid Spas and Hot Tubs
Flush House if Vacant (Second Homes)

## Slide 10: Reducing OPPP Exposure - 3
Drain Water Heater Monthly
Substitute Well Water for Piped Water
Install Showerheads with Filters
Install Tap Filters
Use Water Bottles with Filters or UV

## Slide 11: Regular Remediation
Drain Water Heater Monthly
Raise Water Heater to 130º F (55º C)
Reduce Stagnant Portions: Flush
Remove All Dead Ends
Point-of-Use Filters and Shower Heads
Remove Aerosol-Generators

## Slide 12: Monitoring OPPs
What to sample; water or biofilm?
What indicator; Escherichia coli or heterotrophic plate count (HPC) don’t correlate with OPPP numbers?
What frequency to monitor?
What OPPP numbers indicate disease risk?

## Slide 13: Green Buildings Enrich OPPP Numbers
Lower Water Heater Temperatures
Longer Water Residence Time
Reduced Flow, Misting Shower Heads
Biofilm Build-Up